## Slide 1: SMART FLOOR CLEANER

## Slide 2
Components required
1)2x 100rpm Geared motors
2) 2x Wheels for motors
3) 2× wheels
4) 1x Arduino UNO
5) 1x HC-05/06 Bluetooth module
6) 1x L293D motor driver board
7) 1x Standard servo motor (180 degree rotation)
8) 1x 12V Sealed lead acid rechargeable battery
9) 1x 12V Water pump
10) 2x TIP31C/TIP122 NPN power transistors

## Slide 3
11) 2x Old CDs
12) Wiping cloth
13) A needle and thread
14) Vinyl tubing
15) Male-male/ female-female/ male- female jumper wires
16) Male/female headers
17) Nuts and Screws
18) Plywood base
19) plastic bottle

## Slide 4
ESTIMATED COST:- 1500-2000

## Slide 5
WORKING
Smart floor cleaner works on Arduino programming. It uses a Bluetooth module. Using the app downloaded from play store (Bluetooth serial control), we can control the motion of the bot. Forward,reverse,left,right, pump-on,off,mop-on,off.For all these motion the essential commands are given in to Arduino board. Smart floor cleaner uses a 12V water pump to pump water in to the mop while cleaning. We can adjust the quantity of water coming out of the tube by the control of mobile device.
The rear side of the bot, there is another mop used to dry the water pumped by the cleaner. It can be controlled anywhere within the range of 6m. The complete components uses 12V battery which can be recharged when required. By increasing efficiency of motor and size of the mop, we could build a larger one for household purposes and other purposes.

## Slide 6
ADVANTAGES
1.High efficiency
2.low cost
3.can be controlled easily
4.Working time can be reduced

## Slide 7: CODE
#include <Servo.h> Servo myServo; int r_motor_n = 10; //PWM control Right Motor + int r_motor_p = 11; //PWM control Right Motor - int l_motor_p = 9; //PWM control Left Motor - int l_motor_n = 6; //PWM control Left Motor + int pump = 4; int mop = 5; int serv = 3; int speedy = 255; int incomingByte = 0; // for incoming serial data | void setup() { myServo.attach(3); myServo.write(0); pinMode(r_motor_n, OUTPUT); //Set control pins to be outputs pinMode(r_motor_p, OUTPUT); pinMode(l_motor_p, OUTPUT); pinMode(l_motor_n, OUTPUT); pinMode(2, OUTPUT); digitalWrite(r_motor_n, LOW); //set both motors off for start-up digitalWrite(r_motor_p, LOW); digitalWrite(l_motor_p, LOW); digitalWrite(l_motor_n, LOW);

## Slide 8
digitalWrite(2, HIGH); Serial.begin(9600); } void loop() { if (Serial.available() > 0) { incomingByte = Serial.read(); } | switch(incomingByte) { case 'S': // control to stop the robot digitalWrite(r_motor_n, LOW); digitalWrite(r_motor_p, LOW); digitalWrite(l_motor_p, LOW); digitalWrite(l_motor_n, LOW); Serial.println("Stop"); incomingByte='*'; break;

## Slide 9
case 'R': //control for right analogWrite(r_motor_n, speedy); digitalWrite(r_motor_p, LOW); analogWrite(l_motor_p, speedy); digitalWrite(l_motor_n, LOW); Serial.println("right"); incomingByte='*'; break; case 'L': //control for left analogWrite(r_motor_n, LOW); digitalWrite(r_motor_p, speedy); analogWrite(l_motor_p, LOW); digitalWrite(l_motor_n, speedy); | Serial.println("right"); incomingByte='*'; break; case 'F': //control for forward analogWrite(r_motor_n, speedy); digitalWrite(r_motor_p, LOW); analogWrite(l_motor_p, LOW); digitalWrite(l_motor_n, speedy); Serial.println("right"); incomingByte='*'; break; break; delay(5000); } }

## Slide 10: MEMBERS
1)HARSHIN HARI
2)JASIRA T P
3)SANGEERTH N K
4)SHAMITH R
5)SHARAN NATH C
6)SHRAVAN SREEDEEP
7)SOORYA P